## Slide 1: Dynamic Host Configuration Protocol (DHCP)
June 23, 2015

## Slide 2: Agenda
DHCP Introduction
How DHCP Works
Initial Message Flow
DHCP Options
DHCP Server Overview
Ipconfig Tool

## Slide 3: DHCP Introduction
The Dynamic Host Configuration Protocol (DHCP) is based on the Bootstrap Protocol (BOOTP) and was built from 1993. which provides the framework for passing configuration information to hosts on a TCP/IP network.
DHCP adds the capability to automatically allocate reusable network addresses and configuration options to Internet hosts
DHCP consists of two components:
a protocol for delivering host-specific configuration parameters from a DHCP server to a host
a mechanism for allocating network addresses to hosts.
DHCP is built on a client/server model, where designated DHCP server hosts allocate network addresses and deliver configuration parameters to dynamically configured hosts.

## Slide 4: DHCP Introduction
A DHCP infrastructure consists of the following elements:
  DHCP servers: computers that offer dynamic configuration of IPv4 addresses and related configuration parameters to DHCP clients.
  DHCP clients: network nodes that support the ability to communicate with a DHCP server to obtain a dynamically leased IPv4 address and related configuration parameters.
  DHCP relay agents: network nodes (e.g., routers) that listen for broadcast and unicast DHCP messages and relay them between DHCP servers and DHCP clients. Without DHCP relay agents, you would have to install a DHCP server on each subnet that contains DHCP clients.
All DHCP messages are sent using the User Datagram Protocol (UDP).
  DHCP servers listen on UDP port 67.
  DHCP client listen on UDP port 68.
  DHCP relay agents listen on both UDP ports

## Slide 5: DHCP Introduction

## Slide 6: DHCP Introduction
Benefits of using DHCP
  Users no longer need to acquire IPv4 address configurations from a network administrator to properly configure TCP/IP.
    When a DHCP client is started, it automatically receives an IPv4 address configuration that is correct for the attached subnet from a DHCP server.
    When the DHCP client moves to another subnet, it automatically obtains a new IPv4 address configuration for that subnet.
  The DHCP server supplies all of the necessary configuration information to all DHCP clients.
    As long as the DHCP server has been correctly configured, all DHCP clients of the DHCP server are configured correctly

## Slide 7: How DHCP Work?
Each time a DHCP client starts:
  it requests IPv4 addressing information from a DHCP server, including:
    IPv4 address
    Subnet mask
    Additional configuration parameters:
      default gateway address,
      Domain Name System (DNS) server addresses,
      DNS domain name,
      Windows Internet Name Service (WINS) server addresses.
  it uses the alternate configuration when it cannot contact a DHCP server (Windows)
    Automatic Private IP Addressing (APIPA) address or an alternate configuration that has been configured manually

## Slide 8: How DHCP Work?
When a DHCP server receives a request:
  it selects an available IPv4 address from a pool of addresses defined in its database (along with other configuration parameters) and offers it to the DHCP client.
  if the client accepts the offer, the IPv4 addressing information is leased to the client for a specified period of time

## Slide 9: Initial Message Flow
Server A
Client
Server B
Client attempts to discover available DHCP servers
DHCPDISCOVER
DHCPDISCOVER
Servers reply with offers
DHCPOFFER
DHCPOFFER
Client collects offers and decides which offer to accept
Client broadcasts request for one of the received offers
DHCPREQUEST
DHCPREQUEST
Server acknowledges client’s use of IP address
DHCPACK
Configuration complete
Client explicitly releases use of IP address
DHCPRELEASE
Graceful shutdown

## Slide 10: Initial Message Flow
Message Type | Description
DHCPDiscover | The first time a DHCP client computer attempts to log on to the network, it requests IP address information from a DHCP server by broadcasting a DHCPDiscover packet. The source IP address in the packet is 0.0.0.0 because the client does not yet have an IP address. The message is either 342 or 576 bytes long—older versions of Windows use a longer message frame.
DHCPOffer | Each DHCP server that receives the client DHCPDiscover packet responds with a DHCPOffer packet containing an unleased IP address and additional TCP/IP configuration information, such as the subnet mask and default gateway. More than one DHCP server can respond with a DHCPOffer packet. The client will accept the first DHCPOffer packet it receives. The message is 342 bytes long.
DHCPRequest | When a DHCP client receives a DHCPOffer packet, it responds by broadcasting a DHCPRequest packet that contains the offered IP address, and shows acceptance of the offered IP address. The message is either 342 or 576 bytes long, depending on the length of the corresponding DHCPDiscover message.
DHCPAcknowledge (DHCPAck) | The selected DHCP server acknowledges the client DHCPRequest for the IP address by sending a DHCPAck packet. At this time the server also forwards any optional configuration parameters. Upon receipt of the DHCPAck, the client can participate on the TCP/IP network and complete its system startup. The message is 342 bytes long.
DHCPNak | If the IP address cannot be used by the client because it is no longer valid or is now used by another computer, the DHCP server responds with a DHCPNak packet, and the client must begin the lease process again. Whenever a DHCP server receives a request for an IP address that is invalid according to the scopes that it is configured with, it sends a DHCPNak message to the client.
DHCPDecline | If the DHCP client determines the offered configuration parameters are invalid, it sends a DHCPDecline packet to the server, and the client must begin the lease process again.
DHCPRelease | A DHCP client sends a DHCPRelease packet to the server to release the IP address and cancel any remaining lease.
DHCPInform | DHCPInform is a new DHCP message type, defined in RFC 2131, used by computers on the network to request and obtain information from a DHCP server for use in their local configuration. When this message type is used, the sender is already externally configured for its IP address on the network, which may or may not have been obtained using DHCP. This message type is not currently supported by the DHCP service provided in earlier versions of Windows NT Server and may not be recognized by third-party implementations of DHCP software.

## Slide 11: Initial Message Flow
DHCP Client State Diagram

## Slide 12: Initial Message Flow
DHCP Message Format

## Slide 13: Initial Message Flow
Operation Code: Specifies the general type of message. A value of 1 indicates a request message, while a value of 2 is a reply message.
  Field Name: Op
  Size: 1bytes
Hardware Type: this field specifies the type of hardware used for the local network. Some of the most common values for this field.
  Field Name: HType
  Size: 1bytes
  1 Ethernet
  6 IEEE 802 networks
length: Hardware address length in bytes. E.g., Ethernet and token-ring both use 6 bytes.
hops: The client sets this to 0. It is incremented by a router that relays the request to another server and is used to identify loops. RFC 951 suggests that a value of 3 indicates a loop.